# HowTo write a new module for iGeoPortal

## Introduction
deegree iGeoPortal is constructed using a complete modular design. Except the central Controller – which is automatically available – and the OLMap module all other components are optional. They can be omitted or replaced by other implementations than the those available from iGeoPortal by default. If a function is required that is not already provided by one of the available modules you can easyly write your own module and configure iGeoPortal (projects) for using it.
There are two different kinds of modules deegree iGeoPortal uses:
- modules including HTML and JavaScript components only
- modules having a server component in addition to the required JavaScript object and HTML page.
Common to each module is its interface. A module's interface is made of a HTML page (from a static or dynamic resource) and a JavaScript object having the same name as the module (consider that the name is case sensitive). A modules JavaScript object must receive a parameter named 'id'. It may receive some additional, but optional, parameters. If an object expects parameters other than 'id' they have to be defined in a module's parameterList when registered to the portal/context (see general iGeoPortal documentation). Each JavaScript object corresponding to a module must implement the two methods paint(...) and repaint(). The paint-method will be called when a iGeoPortal project is initially loaded. The repaint-method will be called every time when the state of the portal has been changed (e.g. by a zoomin or a context-loading). One can force calling the repaint-methods of all registered modules by calling the controllers repaint-method ( [parent.]controller.repaint() ).
This is an example for a valid JavaScript object being part of the MenuBarTop module:
function MenuBarTop (id) {
this.id = id;
this.paint = paint;
this.repaint = repaint;
function paint(targetDocument, parentNode) {}
function repaint() {}
}
Note that the paint-method receives two arguments. Because 'paint' probably will be realized as a set of DHTML-operations manipulating the modules DOM object (document) a reference to it must be passed. The first passed parameter is a reference to the DOM object (document of the modules HTML-page) the content should be painted to. The second is a reference to the documents element underneath DHTML operations shall be performed (just to be used by some special modules).
In the following we will develop a small example that demonstrates the principle idea behind iGeoPortal modules.

## What we like to do
First we must specify what kind of module we want to create, what kind of functionality it should of and how it should be used.
The idea is to have a module for calculating a route between wo given locations using an already existing and freely available routing service. OK, this sounds easy; just take http://www.yournavigation.org/ and every thing is fine. Unfortunately we have to consider a few things:
1. Do we like to have routing just for cars or will we support other means of transportation like bicycles, foot?
2. Do we just like to find the fastest route or do we offer finding the shortest?
3. How a use must enter start and end point? By clicking into the map? By enter location names? By entering coordinates?
4. Will we support additonal way points?
5. Will we just display routes on a map or do we also offer some description and additional information?
6. Will a user be able to download a route as a PDF document, a KMLfile or a GPX track for example?
To demonstrate different aspects of developing a new module we will realize most of the options listed above except 'Downloding a route'. But if you like you can take this a kind of exercise you can do for yourself.
## How shall it behave/look like
After we have a coarse defintion of functionality we like to have for our module we must concretize workflows and graphical user interface for controlling functionality.
To simpliy usage it will be a good idea to reduce required user interaction to a minimum; this mean: a user just have to enter a start and an end point for the route all other parameter/options will be set to meaningful default values. To enter start and end point a user can enter a geographic name (like Berlin, Proskauer Strasse) or enter geographic coordinates (WGS84, like 6.3265/52.6452) or klick into the map. For last option he first have to select if he likes to enter the start or the end point; as default start point will be entered.
At this point we can define that we need a GUI containing a map (will provided by iGeoPortal as default and so can be ignored here) as well es elements for entering start and end point. Because we also like to force calculation of the route we need a button for it and it probably is a good idea to have a further button to clear the form. It also might be useful to enable calculation of reverse route, so we will introduce a third button. Using this information our GUI possibly looks like this:

Next we have to consider that a use may likes to add some additional way points to force using a specific route. Because every way point possibly turns out to be useless we must support removing them.

Now this already looks nice, but what's about options for calculating routes mentioned above? For this we will add some Radiobuttons for selecting calculation of fastest or shortest route and a drop-down-list for selecting transportation means:

Looks like we have finished specification of GUI elements for defining parameters for calculating a route. But what's about presenting the result. OK, we want to see the route within the map, and we also want the map module to zoom to the extent of the route. But we also defined that we want to offer some description and additonal information about calculated route.
Because the GUI already contains a lot of elements we suggest introducing tabs to assure a clear arrangement. Beside some general description of the route we like to display the overall length of the route, the number of OSM nodes and – if we have defined some way points - the length of each route segment.

## How it works
After we have defined what our module shall do, how it looks like and how it behaves we now must spend some thoughts on how this will be realized. From a technical point of view a few things must be considered:
- iGeoPortal uses MVC-pattern, which means we have a clear seperation between view (GUI), application logic and data model.
- Simple parts of the application may be implemented client side using JavaScript; more complicated application logic should be delegated to the server side of iGeoPortal.
- For implementing the view parts of our module we suggest using extJS framework
- For communiation between browser and server usage of AJAX and JSON is strongly recommented.
In case of our routing-module we assume calculation of the route is the complicated part of the job and so we will be delegated to the server. But if we have a closer look on how we have defined behavior of the GUI we find another compliated part. Remember: we defined that a user may enters a geographical name for start, end and way points. Such a name must be resolved by a gazetteer to retrieve geographic coordinates required by the YourNavigation routing service. At a first look this seems not to require an additional server sided operation, we just can send the names when we start route calculation and the server will find coordinates e.g. by using nomanitim.
But this will cause two problems:
1. We like to see our start-, end- and way-points in the map even before we have calculated a route.
2. What's to do if the geographic name, a user has entered, is ambiguous or it does not exist within our gazetteer?
So, after a user has defined a point by a geographic name our module must ask a gazetteer to validate that a place with the entered name exists and that the name is unambiguous. Because this is a little bit complicated if it will be done within a browser we will delegate it to the server. If our according server sided component finds out that a name is ambiguous or it does not exists the user must be informed and requested to enter a new name or – if the name is ambiguous - select the one he intends.
We can conclude: two sever sided components are requiered. One for validating geographic names and one for calculating a route.
## How it is implemented
There is no fixed rule that says that we have to start implementation on the client (browser) or on the server side. Both ways are possible and there are reasons for both of them. To avoid an extending discussion of advantages for this and disadvantages for that we simply define that we will start with the client side.
### General aspects
Since implementation of the client/browser side will require us do write a few hundred lines of code and HTML which will contain a lot of stuff that is not very specific for iGeoPortal we will do not present the complete code here, we just focus on the important parts.
As already has been pointed out at least we need a HTML/JSP page and a JavaScript object having the same name as our module. So we first create a new sub dirctory under the modules directory of iGeoPrortal with name 'routing'; within this directory we create a JSP page named routing.jsp and a javascript file named routing.js. Within routing.js we create a template for our module object:
function Routing(id) {
this.id = id;

this.paint = paint;
this.repaint = repaint;

function paint(targetDocument, parentNode) {
// TODO
}

function repaint() {
// TODO
}
}
Our JSP page must use UTF-8 encoding and must import some CSS style sheet and java script libraries to support extJS and deegree styling.
<%@ page language="java" contentType="text/html; charset=UTF-8" pageEncoding="UTF-8"%>
<!DOCTYPE html PUBLIC "-//W3C//DTD HTML 4.01 Transitional//EN" "http://www.w3.org/TR/html4/loose.dtd">
<html>
<head>
<meta http-equiv="Content-Type" content="text/html; charset=UTF-8">
<meta name="author" content="lat/lon GmbH" />
        <meta name="KeyWords" content="deegree iGeoPortal lat/lon" />

        <link href="../../css/deegree.css" rel="stylesheet" type="text/css" />
        <link rel="stylesheet" type="text/css"
href="../../javascript/ext-3.3.1/resources/css/ext-all.css" />
        <link rel="stylesheet" type="text/css" title="blue"
href="../../javascript/ext-3.3.1/resources/css/xtheme-blue.css" />
        <link rel="stylesheet" type="text/css" title="gray"
href="../../javascript/ext-3.3.1/resources/css/xtheme-gray.css" />
        <link rel="stylesheet" type="text/css" title="black"
href="../../javascript/ext-3.3.1/resources/css/xtheme-access.css" />
        <link rel="stylesheet" type="text/css" title="wpt"
href="../../css/wpt/ext-3.3.1/css/ext-all.css" />
        <link rel="stylesheet" type="text/css" title="nds"
href="../../css/nds/NDS/ext-all.css" />

        <script type="text/javascript"
src="../../javascript/ext-3.3.1/adapter/ext/ext-base.js"></script>
        <script type="text/javascript"
src="../../javascript/ext-3.3.1/ext-all.js"></script>

        <script type="text/javascript">

        function register() {
        if ( parent.controller == null ) {
        parent.controller = new parent.Controller();
        parent.controller.init();
        }
        parent.controller.initRouting( document );
        parent.setActiveStyleSheet();
        }

        </script>
</head>
<body onload="register();" onunload="parent.controller.vRouting.kill();">
</body>
</html>
Notice that we catch the onload event to invoke the method register() that will register the main DOM document of our JSP/HTML page to the central controller – after it is ensured that the controller is initialized. After this the method parent.setActiveStyleSheet() is invoked to set the current (extJS) style. We also catch the onload event for cleaning up a few this; for this we must ad the method kill() the modules object.
function Routing(id) {
this.id = id;

this.paint = paint;
this.repaint = repaint;
this.kill = kill;

function paint(targetDocument, parentNode) {
// TODO
}

function repaint() {
// TODO
}

function kill() {
// TODO
}
}
After we have created the two files everything iGeoPortal requires for registering a module is available. So we can extend our configuration by adding the routing module to the west-area of our starting project (wmc_start_utah.xml).
<deegree:Module hidden="false" type="content" width="350" height="600"
        header="false" top="42" left="510" scrolling="auto">
<deegree:Name>Routing</deegree:Name>
<deegree:Content>./modules/routing/javascript/routing.jsp</deegree:Content>
<deegree:ModuleJS>./modules/routing/javascript/routing.js</deegree:ModuleJS>
</deegree:Module>
After reloading the project we will see an additional accordian area in the west area named 'Routing' without any content.
### The GUI
Even if this is a first success it's a little bit less functionality for a routing module so we have to add some extJS elemtents to create a GUI as defined above. Since this is not specific for iGeoPortal it will not be explained in detail how this works. Even if you are free to include JavaScript code for creating the GUI into routing.jsp we suggest creating a new JavaScript file within the modules/routing/javascript directory named gui.js that will contain a class named RoutingGUI that provides all of the GUI creation and handling methods. To register gui.js for our routing module we must enhance the registration of the module within our project:
<deegree:Module hidden="false" type="content" width="350" height="600"
        header="false" top="42" left="510" scrolling="auto">
<deegree:Name>Routing</deegree:Name>
<deegree:Content>./modules/routing/javascript/routing.jsp</deegree:Content>
<deegree:ModuleJS>./modules/routing/javascript/routing.js</deegree:ModuleJS>
<deegree:ModuleJS>./modules/routing/javascript/gui.js</deegree:ModuleJS>
</deegree:Module>
The GUI will be initialized within the paint()-method of Routing class that will be invoked by the central controller when the module is loaded.
function paint(targetDocument, parentNode) {
var tmp = window.location.pathname.split('/');
var s = '';
for ( var i = 0; i < tmp.length - 1; i++) {
s += (tmp[i] + '/');
}
this.url = window.location.protocol + '//' + window.location.host + s +
        'ajaxcontrol';

// init module's GUI
this.gui = new RoutingGUI();
this.gui.initGUI();

this.initMarkers();
}
As you see before initializing the gui object and invoking its initGUI() method we first determine the base URL of the AJAX controller of iGeoPortal and store it within an instance variable named this.url. This enables us accessing the server sided AJAX controller from any place within the routing module/class. After initializing the GUI we invoke a method named this.initMarkers() that is also part of the Routing class and that is responsible for initializing a special layer within the map module (OpenLayers) that will contain/show markers of start-, end- and way-points of our desired route.
function initMarkers() {
var olmap = controller.getFrame('IDOLMap');
this.markers = new olmap.OpenLayers.Layer.Markers( "Markers" );
controller.vOLMap.getMap().addLayer( this.markers );
}
The important part is given in the first statement of the method. Using the controllers method getFrame(..) we can access the frame of each module registered to iGeoPortal – remember: iGeoPortal handle module GUIs by creating on iFrame for each module. If we are required to access or create new objects within other modules we must use the scope of this module!
As already explained we will not give a complete description of the code for creating the GUI but a few things have to be explained when writing a module for iGeoPortal. For this we will have a look at the iniGUI() method of class RoutingGUI:
function RoutingGUI() {

// GUI messages and labels
this.messages;
// frame of the routing module
this.routingFrame = controller.getFrame('IDRouting');
[. . . .]

//GUI handling/creation methods
this.loadMessages = loadMessages;
this.addControlPanel = addControlPanel;
this.addInformationPanel = addInformationPanel;
[. . . .]

function initGUI() {
this.routingFrame.Ext.QuickTips.init();

// load messages for language specific text/lables
this.loadMessages();

var messages = this.messages;
var rootPanel = new this.routingFrame.Ext.TabPanel( {
region : 'center',
border : false,
bodyBorder : false,
activeTab : 0,
items : [ {
id : 'tabControlPanel',
border : false,
bodyBorder : false,
title : messages['IGEO_ROUTE_TAB1'],
layout : 'border'
}, {
id : 'tabInfoPanel',
border : false,
bodyBorder : false,
title : messages['IGEO_ROUTE_TAB2'],
layout : 'border'
} ]
});

this.addControlPanel();
this.addInformationPanel();

new this.routingFrame.Ext.Viewport( {
id : 'VIEWPORT',
layout : 'border',
items : [ rootPanel ]
});
}

[. . . .]
}
At first we see declaration of some instance variables; this.routingFrame holds a reference to the frame of the routing module where the GUI elements will be located; this.messages will store all message and label strings of the GUI and will be explained later.
Within the initGUI() method we first invoke extJS method for enabling tooltips; after this a method named loadMessages() will be called. This method contains code for loading language specific messages from the server enabling us to have a french, german or english GUI depending on the configured language of the browser. The loadMessages() method looks like this:
function loadMessages() {
// create bean containing all required messages
var bean = JSON.stringify(new function() {
this.action = 'getMessages';
this.keys = [ 'IGEO_ROUTE_TAB1', 'IGEO_ROUTE_TAB2' ];
}, null, false);

// send request/bean to the server part of the module
var tis = this;
try {
submitPostRequest(this.url, function(result) {
tis.messages = JSON.parse(result);
}, bean, null, false);
} catch (e) {
alert(22 + JSON.stringify(e) + this.url);
}
}
For loading the messages we use a standard mechanism implemented in iGeoPortal. At first we have to create a JSON object representing our request to the server. The value of the mandatory field 'this.action' is the name of the server sided method we like to invoke. The method 'getMessage' is one of the server sided methods not depending on a specific module and that enables us accessing deegree's i18n package. The value of the element 'this.keys' must be an array containing the list of keys of strings we like to read from deegree's i18n package. At the moment just the two keys 'IGEO_ROUTE_TAB1','IGEO_ROUTE_TAB2' will be requested. In the file org.deegree.i18n.messages_en.properties we have assigned following values to these keys:
#routing module
IGEO_ROUTE_TAB1=control
IGEO_ROUTE_TAB2=result information
If you are running your browser in an other language than english you have to add adequate entries into the properties file assigned to your language.
After we have defined the JSON object we pass it to the server using an AJAX mechanism by invoking a method named submitPostRequest(..). This method is defined in file $igeoportal home$/javascript/request_handler.js.
1. First parameter is the URL the will be target of our request – just accept this for the moment, we will explain later where the get this URL.
2. The second parameter is a callback-function that will be invoked when the result from the server has been returned; here you have to add your code that handles the result.
3. The third parameter is our JSON object contained the request that shall be performed.
4. The forth parameter is null but it can be used to set some specific header fields (if useful)
5. And the last parameter which is of type boolean indicates if a request shall be executed asynchronouly (true) or synchronously (false). In this case we decided to use synchron request processing because as long a messages and labels are not available we can not built our GUI.
You will find this mechanism of AJAX request handling in most of the modules of iGeoPortal that uses some server sided functions. Just a few older modules still uses another mechanism that can be ignored here.
If we now go back to the initGUI() method after loading the messages we can start creating our GUI by adding a TabPane with two tabs. The names/titles of the tabs will be set by assigning the according values from the messages we had read just before. This kink of mechanism for handling messages is common for all iGeoPortal modules that uses extJS GUIs that are defined within a seperate JavaScript file.
As an alternative it would be possible to use direct access to deegree's i18n package if the extJS GUI code will be implemented within the module's JSP page. Have a look at the easygaz module for example to see how it works. To keep the main JSP page cleaned up and still enable direct access to deegree's i18n package it also would be possible to exclude extJS GUI-code into specialized JSP pages which can be included using <jsp:include> tags.

But as already said you may chose your own way of implementating the GUI. For futher description of the routing module we will go on using extJS GUI defined in its own JavaScript class and file. For details of the implementation please have a look at ./modules/routing/javascript/gui.js as it comes with iGeoPortal demo as well as demo and API pages for extJS (3.4) available from www.sencha.com.
### GUI Event Handling
For controlling the application logic described below and changes to the GUI itself we have to catch some events. As alrady said, we created our GUI using extJS, so it looks like this:

As you can see there are a lot of elements that fires event that we have to deal with. To seperate event handling and GUI creation we decided to introduce a special class named RoutingGUIActionHandler that is implemented in a JavaScript file named actionhandler.js. All events, except a few simple ones, that just changes the GUI itself and those setting iGeoPortal into a new mode/state, will be delegated to this class.
Let's start with buttons at the left of the text fields. If you press one of them the application will change its mode/state for catching mouse clicks onto the map and entering coordinates of the click point into the text field assigned to button that is pressed (see end point in example above).
var tis = this;
var btStart = new this.routingFrame.Ext.Button( {
id : 'btStart',
enableToggle : true,
x : 10,
y : 30,
tooltip : tis.messages['IGEO_ROUTE_STARTPTN_TOOLTIP'],
icon : './images/flag_green.png',
handler : function(toggled) {
if (toggled) {
tis.resetStates(this);
parent.controller.vRouting
.setStatePerformed('selectStartPoint');
}
}
});
From the code fragment above you can see that we create a new toggle button within the scope of the routing module. We catch the button-pressed event by registering a handler-function to the button. Each time the button will be pressed, the handler function will be invoded with parameter toggled == true. In this case first a method named resetStates(..) will be invoked that unpresses all other toggle buttons of the routing module. After this the setStatePerformed method of the routing module will be invoked to set set iGeoPortal to 'selectStartPoint'-state/mode.
function setStatePerformed(state) {
this.state = state;
// use this object a handler for click events fired by the map
// by assigning it a mode to the controller
controller.mode = this;

}
As you can see, just the internal variable state of the routing module will set and the routing module itself will be set to the controller.mode (in next chapter we will explain what this does mean).
Next we will have a look at the text fields. As explained above we will enable users to enter names of geographic locations but we can not be sure that these locations realy exists (in our gazetteer) or that a name in unambigous. So, after a users has entered a name we must validate it. To determine that user has finished entering a geographic name we will catch the lost-focus (blur) event of the textfields. This means: every time a text field loses its focus we assume that a user finished entering a geographic name. Let's see how it works:
var tfStart = new this.routingFrame.Ext.form.TextField( {
id : 'tfStart',
x : 40,
y : 30,
anchor : '95%',
onBlur : function(event, textfield) {
tis.actionHandler
.solveGeographicNamePerformed(event, textfield);
}
});
As you things are similar to handling of toggle buttons describe above, but instead of registering a handler we now catch the onBlur event. Because in this case some more compliacted things must be done we delegate event handling to our envent handler class by invoking its solveGeographicNamePerformed method.
function solveGeographicNamePerformed(event, textfield) {
if ( textfield.value == null || textfield.value == '' ) {
// nothing to do because the use did not enter something
return;
}

if ( !this.isCoordinates( textfield.value ) ) {
// if the value of a text field is not a pair of coordinates we have
// to ask the server for checking if it's a valid geographic name
var bean = JSON.stringify( new function() {
this.action = 'checkGeographicName';
this.QUERYSTRING = textfield.value
}, null, false );
try {
        var result = submitPostRequest( gui.url, function(result) {}, bean,
        null, false );
        this.handleCheckGeographicName( result, textfield );
       } catch(e) {
        alert( 5 + " " + e );
       }
} else {
var coords = this.getCoordinates( textfield.value );
this.createWaypoint( textfield.id, textfield.value, coords[0],
        coords[1], -9E9, -9E9 );
}
}
First we must check if a user realy has entered a value, otherwise we leave the method immediately. Next thing we have to check is wether or not a user has entered a geographic name or geographic coordinates. If a user has enter just coordinates we have to parse the coordinates from the text field ( this.getCoordinates(..) ) and create a new way point to be used for route calculation. Otherwise, this means a user has entered a geographice name, we must validate this name asking a server sided listener. The general mechanism of this already has been explained for loading messages. We create a JSON object and send it to the server using a synchonous HTTP Post request. The result of this request will be passed to a method named handleCheckGeographicName that performs required actions depending on the result content.
If no exception occurs the result content will always be a list of 0..n arrays where each array looks like this:
geographic name | lat/lon x coordinate | lat/lon y coordinate | x coordinate in map CRS | x coordinate in map CRS
Three situations are possible:
1. no matching geographic name could be found within the gazetteer: This is easy because we just have to inform a user about this.
2. exactly one matching geographic name has be found within the gazetteer: Thisis the best situation because do not have nothing to do
3. more than on matching geographic name has be found within the gazetteer: This is the most complex situation because we must offer a dialog to a user for selecting the location he intents. Let's see how the code for this looks like.
   function handleCheckGeographicName(result, textfield) {

    var messages = this.gui.getMessages();
    var items = JSON.parse( result );
    [...]
    var store = new Ext.data.ArrayStore({
        data : items,
        fields : ['name', 'p1', 'p2', 'p3', 'p4']
    });

var combo = new Ext.form.ComboBox({
       store : store,
       displayField : 'name',
       width	: 500,
       x	: 10,
       y	: 15,
       mode : 'local'
   });
var tis = this;
var btOK = new Ext.Button({
  x: 10,
      y: 55,
      height: 25,
      width: 30,
      tooltip: messages['IGEO_ROUTE_SELECT_GEOGRNAME_OK_TT'],
      text: messages['IGEO_ROUTE_SELECT_GEOGRNAME_OK'],
      handler: function(button, event){
var idx = store.find('name', combo.getValue() );
// fill text field with selected value/location
textfield.value = items[idx][0];
// WGS 84 coordinate
var x1 = parseFloat( items[idx][1].split(' ')[0] );
var y1 = parseFloat( items[idx][1].split(' ')[1] );
// coordinate using CRS of current map
var x2 = parseFloat( items[idx][2].split(' ')[0] );
var y2 = parseFloat( items[idx][2].split(' ')[1] );
// create a new route point object for select value
var routePoint = tis.createRoutePoint( textfield.id,
        items[idx][0], x1, y1, x2, y2 );

        controller.vRouting.updateRoutePoint( routePoint );
button.ownerCt.close();
}
});
var btCancel = new Ext.Button({
      x: 50,
      y: 55,
      height: 25,
      width: 60,
      tooltip: messages['IGEO_ROUTE_SELECT_GEOGRNAME_CANCEL_TT'],
      text: tis.gui.messages['IGEO_ROUTE_SELECT_GEOGRNAME_CANCEL'],
      handler: function(button, event){
textfield.value = '';
button.ownerCt.close();
}
});
var w = new Ext.Window({
        title : messages['IGEO_ROUTE_SELECT_GEOGRNAME_TITLE'],
        height : 120,
        layout : 'absolute',
        width	: 530,
        bodyStyle : 'padding: 5px',
        modal	: true,
        items : [combo, btOK, btCancel]
      });
w.show();

      [...]
First we must parse the result – which is a list of arrays as a JSON object - to transform it into a JavaScript object. After this we create an ExtJS data store that wraps the result. After this we create a combo box using the data store we just created before. We also define that data field 'name' shall be displayed within the combo box.
Notice that we do not use the scope of the routing module for creating ExtJS objects at this place; this is because we want to display the dialog on top of the complete iGeoPortal and not just as part of the module's GUI.

Next we define a OK-button with a handler saying what to do incase a user has chosen a geographic name from the combo box. The handler is implemented as an inline function that first reads the selected item and after this it creates a new RoutePoint from it that will be passed to the routing module for futher processing. Notice that the ID of the text field will be used as ID for the route point! This enables the routing module to create an assoziation between. At least the dialog will be closed. The cancel button looks the same but with a simpler implementation of the handler function. It just clears the assigned text field and closes the dialog. At least we create a modal window and add the combo box and both buttons; the result looks like this:

We will skip description for handling transportation combox, clear and reverse button because there is no magic or complicated things to do. The only realy interesting thing left to do is finding a route. This will be triggered when pressing the 'find route' button.
var btFind = new this.routingFrame.Ext.Button( {
id : 'findRoute',
x : 10,
y : 125,
height : 25,
width : 70,
tooltip : messages['IGEO_ROUTE_FIND_BT_TT'],
text : messages['IGEO_ROUTE_FIND_BT'],
handler : function(button, event) {
try {
controller.vRouting.findRoutePerformed(button, event);
} catch(e) {
Ext.Msg.show({
title: messages['IGEO_ROUTE_FIND_ERROR'],
msg: e,
buttons: {ok:
        messages['IGEO_ROUTE_FIND_BT_OK'] },
width: 300,
icon: Ext.MessageBox.ERROR
});
}
}
});
As you can see the handler function of the 'find route' button (implemented in RoutingGUI) just triggers findRoutePerformed method of routing module – we will explain how finding a route works in next chapter. If this method terminates with an exception a message window will pop up giving some information about what went wrong (Notice that the message window will be opened in scope of the basic iGeoPortal frame and not within the routing module).
### The application logic
The application logic is encapsulated within class Routing; we already saw its basic structure above. To do some real work we must enhance it a bit. See following code fragment listing all declared/implemented instance variables and methods:
function Routing(id) {
this.id = id;
this.url;
this.markers;
this.routeLayer;
this.state;
this.url;
this.gui;
/**
* store current markers
*/
this.markerArray = new Array();
this.markerArray[0] = new Object();

this.addMarker = addMarker;
this.drawRoute = drawRoute;
this.findRoutePerformed = findRoutePerformed;
this.initMarkers = initMarkers;
this.kill = kill;
this.onClick = onClick;
this.onDbClick = onDbClick;
this.paint = paint;
this.removeMarker = removeMarker;
this.removeAllMarkers = removeAllMarkers;
this.repaint = repaint;
this.setStatePerformed = setStatePerformed;
this.getUrl = getUrl;
this.updateRoutePoint = updateRoutePoint;
this.validateCalcRouteRequest = validateCalcRouteRequest;
...
We alread learned about behavior of methods paint(..), repaint() and kill(). Two further methods are declared to make the class be usable for a specific behavior of iGeoportal. These methods are onClick(..) and onDbClick(..). A class implementing these methods can be registered as a state/mode object to iGeoPortals controller – you rember when we explained how the btStart button works? We invoked the setStatePerformed method when the button has been pressed and set this routing object to the controller.mode. The current state/mode object will be informed about any mouse click onto the map. While onDbClick(..) just comsumes the according event without doing anything onClick(..) implements some logic to set coordinates for start-, end- and way-points. Let's have a look at it:
function onClick(e) {
if (this.markers == null) {
this.initMarkers();
}
var x = controller.gtrans.getSourceX(e.xy.x);
var y = controller.gtrans.getSourceY(e.xy.y);
var iconURL;
var routing = controller.getFrame('IDRouting');
var markerID;
if ( this.state == 'selectStartPoint' ) {
iconURL = this.url + '/../modules/routing/images/flag_green.png';
this.gui.setStartPoint( new RoutePoint(1000, 'start', x + '/' + y,
        -9E9, -9E9, x, y) );
markerID = 1000;
} else if (this.state == 'selectEndPoint') {
iconURL = this.url + '/../modules/routing/images/flag_red.png';
this.gui.setEndPoint( new RoutePoint(1001, 'end', x + '/' + y, -9E9,
        -9E9, x, y) );
markerID = 1001;
} else {
markerID = this.state;
iconURL = this.url + '/../modules/routing/images/flag_blue.png';
var wayPoints = this.gui.getWayPoints();
for ( var i = 0; i < wayPoints.length; i++) {
if (wayPoints[i].id = this.state) {
wayPoints[i].xlocal = x;
wayPoints[i].ylocal = y;
wayPoints[i].text = x + '/' + y;
break;
}
}
this.gui.setWayPoints( wayPoints );
}
this.removeMarker(markerID);
this.addMarker(markerID, x, y, iconURL);
}
After we have ensured that a OpenLayers layer for handling markers for start-, end- and way points has been initialized (initMarkers()) we read out the coordinates of the mouse click point expressed in coordinate reference system of the map. After this we have to check which kind of coordinates a user asked for. This can be find out by having a look at the state ouf the routing module. As you can see from code abovehandling of start- and end-point is very similar. At first an icon will be set and after this the start/end point will be created by setting coordinates of the click point. Because we do not know values for according WGS84 coordinates we set them to -9E9. The create RoutePoint will be registered as start/end point to the GUI where its value (third parameter) appears within the according text field.
For way points thing are a little bit different because when creating a new set of input elements for a way point in the GUI an new RoutePoint automatily will be created. So, when a user defines location of a way point by clicking into the map, first the according way point must be read from the array of way points stored in RoutingGUI. This can be done by comparing the ID of a way point with the state of the routing module! If the according way has been found we must adapt its local coordinates and the text that shall be displayed within the according text field.
For all three types of route points a so called marker ID will be created. This will be used to idnetify an already existing marker when it should be removed from the map. Because start- and end-point always will have the same marker id and way points uses an increasing counter to create its marker ID (waypoint.ID == state.ID == marker.ID) markers easyly can be handled within an assoziative array. To add a new marker within the onClick method we first invoke removeMarker method to remove the marker with the same ID as the one we just have created (if it exists). After this the addMarker method will add a new marker to the map at position assigned to according route point using an icon depending on type of this point.
At next we will have a look what happens when a user presses the 'find route' button. In the chapter 'GUI Event handling' we saw that the handler of the according button just delegates event handling to the findRoutePerformed() method of routing module. Let's see how this method is implemented.
function findRoutePerformed(button, event) {
var routing = controller.getFrame('IDRouting');
var wp = new Array();
var wpLocal = new Array();
var wayPoints = this.gui.getWayPoints();
for ( var i = 0; i < wayPoints.length; i++) {
wp.push( [ wayPoints[i].x, wayPoints[i].y ]);
wpLocal.push( [ wayPoints[i].xlocal, wayPoints[i].ylocal ]);
}

var tmpGUI = this.gui;
// will throw an exception if request is not valid
this.validateCalcRouteRequest( tmpGUI.getStartPoint(),
        tmpGUI.getEndPoint() );
var bean = new function() {
this.action = 'calculateRoute';
this.transportation = routing.transportation;
this.fastest = routing.Ext.getCmp('rdfastest').getValue();
this.startText = tmpGUI.getStartPoint().text;
this.endText = tmpGUI.getEndPoint().text;
this.startWGS84x = tmpGUI.getStartPoint().x;
this.startWGS84y = tmpGUI.getStartPoint().y;
this.endWGS84x = tmpGUI.getEndPoint().x;
this.endWGS84y = tmpGUI.getEndPoint().y;
this.startLocalx = tmpGUI.getStartPoint().xlocal;
this.startLocaly = tmpGUI.getStartPoint().ylocal;
this.endLocalx = tmpGUI.getEndPoint().xlocal;
this.endLocaly = tmpGUI.getEndPoint().ylocal;
this.wp = wp;
this.wpLocal = wpLocal;
};

var s = JSON.stringify(bean, null, false);
var tis = this;
submitPostRequest(this.url, function(result) {
if (result.indexOf('ExceptionBean ') > -1) {
alert(result);
} else {
tis.drawRoute( JSON.parse( result ) );
}
}, s, null, false);
}

The first half of the method contains statements for creating a JSON object to be send to the server for calculating the route. Just before the request bean will be initialized we check if start- and end-point has been set with valid values (validateCalcRouteRequest()). After this we again perfrom a AJAX request against the server just the way we already desribed. Incase the server returns an exception a message will be displayed otherwise the result will be parsed and handling will be delegated to drawRoute method.
The drawRoute method is not so complicated because we decided to draw routes on the server side as a kind of dynamic WMS layer (see below for details).
function drawRoute(routeDescription) {
if ( controller.mapModel.getLayerByName( 'highlight' ) != null ) {
this.removeRoutingLayer();
}

var env = new Envelope( routeDescription.bbox[0], routeDescription.bbox[1],
        routeDescription.bbox[2], routeDescription.bbox[3]);
env = env.getBuffer( env.getHeight() );
controller.actionPerformed( new Event( this, "BBOX", env ) );

this.addRoutingLayer();
this.gui.setDescription( routeDescription.description );
this.gui.setLength( routeDescription.distance );
this.gui.setNumberOfNodes( routeDescription.numberOfNodes );
}
At first we remove a layer named 'highlight' if it already exists. After this we read out the bounding box of the route from the route description retruned by the server sided route calculating listener; we a buffer and zoom our map to the resulting envelope by fireing a BBOX-event. Next we a the layer containing our route to the maps data model (this.addRoutingLayer()) and set descriptions of the route to accoring GUI elements.
The most interesting question at this point is: Why and how can we add a route as a 'normal' WMS layer to our map?
To answer this, first have a look at the addRoutingLayer() method:
function addRoutingLayer() {
 // get URL of deegree session WMS
        var tmp = window.location.pathname.split( '/' );
        var s = '';
        for ( var i = 0; i < tmp.length-1; i++) {
        s += (tmp[i] + '/' );
        }
        var layers = new Array();
        layers[0] = new Object();

        layers[0]['name'] = 'highlight';
        layers[0]['title'] = 'route';
        layers[0]['queryable'] = false;
        layers[0]['metadataURL'] = null;
        layers[0]['minScale'] = '0';
        layers[0]['maxScale'] = '99999999999';
        layers[0]['visible'] = true;
        var wmsurl = window.location.protocol + '//' + window.location.host + s +
        'highlightwms';
        controller.addLayersToModel( "route highlight", wmsurl, "1.1.1", layers,
        "image/png", false, true );

  controller.vOLMap.getMap().addLayer( this.markers );
}
The trick is using deegree's session WMS. When calculating a route on the server side the according listener not just sends back some information about a route back to the client it also stores the geometry of a route in the user's session using the keyword: TEMP_WMS_GEOMETRY (we will give a detailed description on this later). The deegree session WMS will read out the parameter and creates an according map; the same mechanism is used with the easygaz module for highlighting the selected geographic entity (that's why the name is named 'highlight' ). This enables us to add a layer named 'highlight' to our map model. The only thing left to do is to get the URL of the session WMS. When you have installed iGeoPortal using the demo the session WMS already is availale from the the same base URL as iGeoPortal but with servlet name 'highlightwms'.
The last statement of the method may looks a little bit confusing because we already added the markers layer to the model. But: when a new WMS layer will be added to iGeoPortal the complete map model will be receated to minimize number of GetMap requests to be performd. During this all non-WMS-layers will be removed from the model – remember: markers is not a WMS layer!
### The server side
On server side we have two listeners doing the jobs that would somehow complicated to do within the broswer. At first we have a listener called ValidateGeographicNameListener that is responsible for validating geographic names entered by users and the second one, named CalculateRouteListener, is responsible for calculating a route. To make these listeners avialable for iGeoPortal we have to register them at iGeoPortals registry for ajax listeners (WEB-INF/conf/igeoportal/ajaxcontroller.xml).
        <event name="checkGeographicName" class="org.deegree.portal.standard.routing.control.ValidateGeographicNameListener">
        <parameter>
        <name>address</name>
        <value>http://open.mapquestapi.com/nominatim/v1/search.php</value>
        </parameter>
    </event>
    <event name="calculateRoute" class="org.deegree.portal.standard.routing.control.CalculateRouteListener">
        <parameter>
        <name>address</name>
        <value>http://www.yournavigation.org/api/1.0/gosmore.php</value>
        </parameter>
    </event>
As you see each listener is assigned to an event that will be fired by the browser side of iGeoPortal by performing an AJAX request as already described. If for example an event with action = checkGeographicName has been fired the actionPerformed(..) method of class org.deegree.portal.standard.routing.control.ValidateGeographicNameListener will be invoked. Each valid listener must concretize an abstract class named org.deegree.enterprise.control.ajax.AbstractListener that defines the abstract method actionPerformed(..). We also see that both listeners has declared a parameter named 'address' that contains the base URL of services for handling geographic names and for route calculation. From the URLs you can see that we use Nominatim Gazetteer and YOURS route calculation service, which both bases on Open Street Map data.
Let's see how it works in Detail ….
ValidateGeographicNameListener
public class ValidateGeographicNameListener extends AbstractListener {

    private static ILogger LOG =
        LoggerFactory.getLogger( ValidateGeographicNameListener.class );

public void actionPerformed( WebEvent event, ResponseHandler responseHandler )
        throws IOException {

...
As already has been noticed ValidateGeographicNameListener extends org.deegree.enterprise.control.ajax.AbstractListener to make it a valid listener for iGeoPortal. First we do – that is common for most classes in deegree – is declaring a logger for this class. Then we start implementing the actionPerformed(..) method that has been declared in abstract class ActionListener.
Implementation of actionPerformed(..) method realizes following steps:
1. read out request and configuration parameters
2. create a request against Nominatim gazetteer service
3. perform request against Nominatim gazetteer service
4. receive the result and parse it as an XML document
5. parse the content of the result document and create response to the client (browser)
6. return response back to the client
Except 5. things are straight forward and not very difficult. So we just have a look how the result to a gazetteer request is parsed and a response to a client is created. A response of the Nominatim gazetteer looks like this:
<?xml version="1.0" encoding="UTF-8"?>
<searchresults timestamp="Mon, 12 Sep 11 06:23:30 -0400"
        attribution="Data Copyright OpenStreetMap Contributors, Some Rights
        Reserved. CC-BY-SA 2.0." querystring="bonn" polygon="false"
        exclude_place_ids="79431420,135063"
        more_url="http://open.mapquestapi.com/nominatim/v1/search?
        format=xml&amp;exclude_place_ids=79431420,135063&amp;
        accept-language=de-de,de;q=0.8,en;q=0.5,
        en-us;q=0.3&amp;q=bonn">
<place place_id="79431420" osm_type="relation" osm_id="62508" place_rank="12"
        boundingbox="50.63252639770,50.77439880379,7.022552490234,7.210649490356"
        lat="50.7057605028141" lon="7.10983309521356" display_name="Bonn,
        Regierungsbezirk Köln, Nordrhein-Westfalen, Bundesrepublik Deutschland
        (Landmasse)" class="boundary" type="administrative"
        icon="http://open.mapquestapi.com/nominatim/v1/images/mapicons/
        poi_boundary_administrative.p.20.png"/>
<place place_id="135063" osm_type="node" osm_id="26373169" place_rank="16"
        boundingbox="50.7244818115,50.7444856262,7.08992694855,7.10992742538"
        lat="50.7344839" lon="7.0999274" display_name="Bonn, Regierungsbezirk Köln,
        Nordrhein-Westfalen, Deutschland, Europa" class="place" type="city"
        icon="http://open.mapquestapi.com/nominatim/v1/images/mapicons/
        poi_place_city.p.20.png"/>
</searchresults>
What we need to extract is the places coordinates (lat/lon) and the name of a place:
        List<String[]> result = new ArrayList<String[]>( 50 );
        HttpSession session = ( (HttpServletRequest) getRequest() ).getSession( true );
        ViewContext vc =
        (ViewContext) session.getAttribute( Constants.CURRENTMAPCONTEXT );
        CoordinateSystem modelCrs =
        vc.getGeneral().getBoundingBox()[0].getCoordinateSystem();
        GeoTransformer gt = new GeoTransformer( modelCrs );
        try {
    NamespaceContext nsc = CommonNamespaces.getNamespaceContext();
        List<Node> nodes = XMLTools.getNodes( xml.getRootElement(), "place", nsc );
        for ( Node node : nodes ) {
        String place = XMLTools.getNodeAsString( node, "@display_name",
        nsc, "" );
        // get location of an object in geographic and map CRS
        double lat = XMLTools.getNodeAsDouble( node, "@lat", nsc, 0 );
        double lon = XMLTools.getNodeAsDouble( node, "@lon", nsc, 0 );
        // location coordinates mst be available in:
        // - WGS84 for route calculation
        // - in CRS of current map model for displaying in the client
        Point point = GeometryFactory.createPoint( lon, lat,
        CRSFactory.EPSG_4326 );
        Point pointMap = point;
        if ( !modelCrs.equals( CRSFactory.EPSG_4326 ) ) {
        pointMap = (Point) gt.transform( point );
        }
        String p = point.getX() + " " + point.getY();
        String pm = pointMap.getX() + " " + pointMap.getY();
        // add location to the result array
        result.add( new String[] { place, p, pm } );
        }
        } catch ( Exception e ) {
        LOG.logError( e.getMessage(), e );
        ExceptionBean eb = new ExceptionBean( getClass().getName(), e.getMessage() );
        responseHandler.writeAndClose( true, eb );
        return;
        }
But just reading a places coordinates is not enough. We must consider that our map propable uses another coordinate reference system (CRS) that EPSG:4326 (WGS84) as it is used by Nominatim. So we must read out the maps CRS by getting the server sided project information from the users session and read out the maps CRS from the projects bounding box. If the current map uses any other CRS than EPSG:4326 we must transform the coordiantes returned from the Nominatim gazetteer into the maps CRS. Just after this is done we write a places name and its coordinates (in ESP:4326 as well as in the maps CRS) as a string array into a list ( result.add(...) ).
Why must we return coordinates in EPSG:4326 as well as in the CRS used by the current map? Please remember what the client have to do with these coordinates. First he must add a marker into the map to inform us about the location of a geographical object – for this we need coordinates expressed in CRS of the current map. Second we like to calculate a route – because YOURS routing service expects us to send start- and end-point of a route in geographical coordinates we need the EPSG:4326 coordinate values.
The result list (containing one string array for each matching location) will be returned to die browser as a JSON object. This will be created automaticly when using responseHandler.writeAndClose( .. ) method; you just have to set the correct mime type and character encoding.
String charEnc = getRequest().getCharacterEncoding();
if ( charEnc == null ) {
charEnc = Charset.defaultCharset().displayName();
}
responseHandler.setContentType( "application/json; charset=" + charEnc );
responseHandler.writeAndClose( false, result );

CalculateRouteListener
As already noticed the CalculateRouteLister is responsible for getting a route between a start- and an end-point. The listener receive the settings a user has made and performs a requests against a YOURS services for calculating a route. Because in opposite to validating a geographic name a request received from the client contains several parameters we decided to map incoming request to a specific request bean for simplification of handlung.
...
 String address = getInitParameter( "address" );
        LOG.logDebug( "request: ", event.getParameter() );
        requestBean = new RequestBean( event.getParameter(), modelCrs );
...
The most intersting part of the request bean is its constructor – the rest is just offering some getter methods.
    RequestBean( Map<String, Object> param, CoordinateSystem modelCrs ) {
        transportation = (String) param.get( "transportation" );
        if ( (Boolean) param.get( "fastest" ) ) {
        fastest = 1;
        }
        startText = (String) param.get( "startText" );
        endText = (String) param.get( "endText" );

        GeoTransformer gt = new GeoTransformer( CRSFactory.EPSG_4326 );

        double x = ( (Number) param.get( "startWGS84x" ) ).doubleValue();
        double y = ( (Number) param.get( "startWGS84y" ) ).doubleValue();
        startWGS84 = new Point2D.Double( x, y );

        x = ( (Number) param.get( "endWGS84x" ) ).doubleValue();
        y = ( (Number) param.get( "endWGS84y" ) ).doubleValue();
        endWGS84 = new Point2D.Double( x, y );

        x = ( (Number) param.get( "startLocalx" ) ).doubleValue();
        y = ( (Number) param.get( "startLocaly" ) ).doubleValue();
        if ( startWGS84.x < -8999999999d ) {
        Point p = GeometryFactory.createPoint( x, y, modelCrs );
        try {
        p = (Point) gt.transform( p );
        } catch ( Exception e ) {
        throw new RuntimeException( e );
        }
        startWGS84 = new Point2D.Double( p.getX(), p.getY() );
        }

        x = ( (Number) param.get( "endLocalx" ) ).doubleValue();
        y = ( (Number) param.get( "endLocaly" ) ).doubleValue();
        if ( endWGS84.x < -8999999999d ) {
        Point p = GeometryFactory.createPoint( x, y, modelCrs );
        try {
        p = (Point) gt.transform( p );
        } catch ( Exception e ) {
        throw new RuntimeException( e );
        }
        endWGS84 = new Point2D.Double( p.getX(), p.getY() );
        }

    }
Why it is so complicated? Just remember: A user has several options to enter start-, end- and way points. So each options must be checked. For example: If a user has chosen to enter start- and end-point by clicking into the map, just coordinates in CRS of the map are defined. If he has chosen to define start- and end-point be entering geographic names EPSG:4326 coordinates are defined as well. Because YOURS routing service service requieres EPSG:4326 coorindates we possibly must transform incoming coordinets.
Using the request bean we now can create and perform a request against YOURS routing service. This and parsing of the response as an XML document looks much like th according part of the ValidateGeographicNameListener. And – same as there – after receiving a response von YOURS we must read the parts that we need.
RouteBean route = null;
        try {
        String xpath =
        "kml:Document/kml:Folder/kml:Placemark/kml:LineString/kml:coordinates";
        String coords = XMLTools.getNodeAsString( xml.getRootElement(), xpath, nsc,
        null );
        if ( coords == null || coords.trim().length() < 5) {
        // this for example can happen if you try to find a route from s
        // omewhere in the middle of the sahara to the middle of the atlantic
        // ocean
        LOG.logWarning( "no route found for defined start-, end- and way
        points" );
        ExceptionBean eb = new ExceptionBean( getClass().getName(),
        "no route found for defined start-, end- and way points" );
        responseHandler.writeAndClose( true, eb );
        return;
        }
        xpath = "kml:Document/kml:description";
        String description = XMLTools.getNodeAsString( xml.getRootElement(), xpath,
        nsc, null );
        xpath = "kml:Document/kml:distance";
        double distance = XMLTools.getNodeAsDouble( xml.getRootElement(), xpath,
        nsc, -1 );
        // create response be to be serialized as JSON object
        route = new RouteBean( modelCrs, coords, description, distance,
        requestBean.getStartText(),
        requestBean.getEndText() );
        // store route geometry in the user's session to be used with deegree
        // SessionWMS for rendering a route
        session.setAttribute( "TEMP_WMS_GEOMETRY",
        WKTAdapter.wrap( route.getCoordinates(), modelCrs ) );
        } catch ( Exception e ) {
        LOG.logError( e );
        throw new RuntimeException( e );
        }
Beside coordinates of a route we like to return a description of a route and the distance from start to end. Because the routing service returns a KML document we have a well known structure that can easyly be parsed using some XPath expressions. We also have to consider that a KML document always uses EPSG:4326 CRS for storing coordinates. To handle all information we extracted from the response KML we have created a special class named RouteBean; it is the counterpart to RequestBean we discussed before.
An important statement is last one within the try-catch-clause. Here we read out the geometry (coordinates) from the response bean and store it within the users sesssion. You remeber? We explained that we can visualize a route by adding a new layer to our map model that points to a layer of deegree's session WMS. And this is this place where we store the geometry to be rendered by the session WMS.
After leaving the try-catch-clause the code is nearly the same as for validating a geographic name. We take the response bean and send it back to the client as a JSON object by invoking deegree's responseHandler.writeAndClose( .. ) method.